## Slide 1
Near Field Scanner: measurement optimization & room correction
Presented by Chloé Corno
IMDEA 2nd year internship defence at Klippel GmbH

## Slide 2: Contents
Introduction
Baffle measurements
Measurement time optimization
Room compensation
Conclusion

## Slide 3: Introduction

## Slide 4: Near Field Scanner
Measurements in the Near Field of devices.
Uses Field Separation to remove the boundaries effects on the measurement.
Visualization of results at any point on the 3D space in the Far Field of the device.
Microphone moves thanks to a robotic arm.
Constant interaction between the acoustic boundaries and the system.

## Slide 5: Near Field Scanner – Measurement flowchart

## Slide 6: Field Separation - Principle
General expression of sound field in spherical coordinates:
Simplified form:
Outgoing sound field
(DUT contribution)
Incoming sound field
(boundaries contribution)
How to separate the outgoing and incoming contributions?

## Slide 7: Field Separation - Principle
Scanning on 2 layers yields
In matrix form:
Performing the inversion leads to the
outgoing sound field:
Results vector
Base functions
Coefficient matrix (out and in)

## Slide 8: Baffle measurements

## Slide 9: Baffle prototype
Baffle
Wooden plate
Speaker
Aim: critical evaluation of the prototype.
Influence of the baffle isn’t important, since it will be removed by field separation.
Does the wooden plate have an impact on the measurement?

## Slide 10: Influence of the baffle
3 dB difference
The baffle vibration’s create cancellation effects.
At the first resonance, there is 3 dB difference between the measurements.
Scan evidences how the plate vibrates in anti-phase with the speaker.

## Slide 11: Grid optimization
Problems with baffle:
Vibration
Acoustic shortcut
Diffraction at edges
If the field separation cannot be applied, using an elliptical measurement grid allows to ease off the baffle effect.

## Slide 12: Grid optimization
Elliptical grid leads to smoother results in low frequency.
After the first cone breakup, the spherical & elliptical grids give the same results.
Measuring closer to the driver allows to avoid most boundaries effect.

## Slide 13: Measurement time optimization

## Slide 14: Principle

## Slide 15: Principle

## Slide 16: Principle

## Slide 17: Measurements – oval speaker
Top/Bottom symmetry dominant
Left/Right single plane symmetry is spoiled by the rocking modes
- +
f = 950 Hz

## Slide 18: Measurements – diagonal speaker

## Slide 19: Room compensation

## Slide 20: Principle

## Slide 21: Compensation by a Near Field measurement

## Slide 22: Compensation by a NFS scan

## Slide 23: Tetrahedral box

## Slide 24: Tetrahedral box

## Slide 25: Tetrahedral box

## Slide 26: Tetrahedral box

## Slide 27: Conclusion

## Slide 28: Conclusion